## Slide 1: Calibrating an Intracranial Pressure Dynamics Model with Annotated Clinical Data--a Progress Report
W. Wakeland1 B. Goldstein2 J. McNames3
1Systems Science Ph.D. Program, Portland State University
2Complex Systems Laboratory, Oregon Health & Science University
3Biomedical Signal Processing Laboratory, Portland State University
This work was supported in part by the Thrasher Research Fund

## Slide 2: Background: Intracranial Pressure (ICP)
Traumatic brain injury often causes ICP to increase
  Frequently due, at least initially, to internal bleeding (hematoma)
Persistent elevated ICP  reduced blood flow  insufficient tissue perfusion (ischemia)  secondary injury  poor outcome
Poor outcomes often occur despite the availability of many treatment options
  The pathophysiology is complex and only partially understood

## Slide 3: Background: ICP Dynamic Modeling
Many computer models of ICP have been developed
  Models have sophisticated logic
  Potentially very helpful in a clinical setting
However, clinical impact of models has been minimal
  Complex models are difficult to understand and use
Another issue is that clinical data often lack the annotations needed to facilitate modeling
  Exact timing for medications, CSF drainage, ventilator adjustments, etc.

## Slide 4: Research Objective
Use an IRB approved protocol to collect prospective clinical data
  Carefully annotate the data regarding timing of therapy and mild physiologic challenges
Use the data to calibrate a computer model of ICP dynamics
Use the calibrated model to estimate patient response to treatment and challenges
Compare model response to actual patient response
Improve the model and the calibration process

## Slide 5: Method: Experimental Protocol
Change the angle of the head of the bed (HOB)
  From 30º to 0º for example, and vice versa
  Such changes directly influence ICP
Change the minute ventilation (VR)
  Clinician adjusts VR to achieve specified ETCO2
  Decreasing ETCO2 (mild hyperventilation) triggers cerebrovascular autoregulatory (AR) response
    Intracranial vessels constrictintracranial blood volume decreasesICP decreases
  Increasing ETCO2 has the opposite effect

## Slide 6: Method: ICP Dynamic Model
Core model logic
  State variables: fluid volumes and AR status
  Estimated parameters: compliance, resistance, hematoma volume and rate, control parameters
  Computed variables: fluid flows and pressures
Six intracranial volumes (state variables)
  Arterial blood (ABV), Capillary blood (CBV)
  Venous blood (VBV), Cerebral spinal fluid (CSF)
  Brain tissue (BTV), Hematoma (HV)

## Slide 7: Method: Diagram showing Volumes & Flows

## Slide 8: Method: Model Logic for Pressures
Total Cranial Volume = ABV+CBV+VBV+CSF+BTV+HV
Intracranial Pressure (ICP)
  = Base ICP  10(Total Cranial Volume–Base Cranial Volume)/PVI
  PVI (pressure-volume index) is the amount of added fluid that would cause pressure to increase by a factor of 10
Arterial, capillary, and venous pressures
  Pab = ICP + (ABV)/(Arterial Compliance)
  Pcb = ICP + (CBV)/(Capillary Compliance)
  Pvb = ICP + (VBV)/(Venous Compliance)

## Slide 9: Method: Model Logic for Cerebrovascular AR
Arteriolar resistance changes in order to maintain needed blood flow rate
  higher resistance = constriction
  Lower resistance = dilation
  Time constant for adjustment process: 2-3 minutes
  Upper and lower bounds
Cerebrovasular AR responds to multiple stimuli
  Changing Metabolic needs (e.g., asleep vs. awake)
  Changing ICP, arterial blood pressure, HOB, and VR

## Slide 10: Results: Clinical Data, HOB Changes

## Slide 11: Results: Clinical Data, ETCO2 Changes

## Slide 12: Results: Model Response to HOB Decrease
Note: Actual ICP data has been low-pass filtered and decimated to remove the pulsatile component
mmHg

## Slide 13: Results: Model Response to HOB Increase
Note: Actual ICP data has been low-pass filtered and decimated to remove the pulsatile component
mmHg

## Slide 14: Results: Model Response to ETCO2 Increase
Note: Actual ICP data has been low-pass filtered and decimated to remove the pulsatile component
mmHg

## Slide 15: Results: Model Response to ETCO2 Decrease
Note: Actual ICP data has been low-pass filtered and decimated to remove the pulsatile component
mmHg

## Slide 16: Discussion: Model vs. Actual Response
Model response to raising HOB is very similar to actual response
Model Response to lowering the HOB is less similar
  This is plausible since lowering HOB increases ICP, and the body has several mechanisms to resist such increases
    Most of these are not included in the current model
Response to ETCO2 changes did not fully reflect the patient’s actual response
  This is not unexpected, for the same reason:
    Reliance on a single cerebrovascular AR mechanism in the model

## Slide 17: Discussion: Summary
A model of ICP dynamics was calibrated to replicate the ICP recorded from specific patient during an experimental protocol
The calculated ICP closely resembles actual ICP
The cerebrovascular AR logic in the model only partially captures the patient’s response to respiration change
Next steps: (1) refine the AR logic in the model (2) use optimization to automate the calibration process (3) predict response