## Slide 1: Modeling Intracranial Fluid Flows and Volumes During Traumatic Brain Injury to Better Understand Pressure Dynamics
W. Wakeland1 J. McNames2 M. Aboy2
D. Hollemon3 B. Goldstein3
1Systems Science Ph.D. Program, Portland State University
2Biomedical Signal Processing Laboratory, Portland State University
3Complex Systems Laboratory, Oregon Health & Science University

## Slide 2: Intracranial Pressure (ICP) Overview
Traumatic brain injury
  Car accidents
  Blunt trauma (hit on the head)
  Falls
Elevated ICP often follows due to
  Swelling
  Hematoma (bleeding)
If elevated ICP persists, insufficient blood flow leads to secondary injury
Clinical challenge:
  Maintain sufficient blood flow
  Keep ICP within safe range (<20 mmHg)

## Slide 3: Treatment Controversies
Poor outcomes are common
  Despite availability of many treatment options
  Often due to secondary brain injury
Pathophysiology of TBI only partially understood
Therapies for pediatric TBI have not been rigorously assessed
  Randomized control studies

## Slide 4: Clinical Application of Model
We are developing a model of ICP dynamics
Cannot measure many variables of interest
  Blood flow
  Cerebral compliance
  Metabolic demand
  Cerebral autoregulation
Our approach
  Create dynamic model with all variables of interest
  Calibrate to patients based on observed variables
    ICP, ABP, CVP, etc.
  Estimate variables of interest with dynamic model
    Cerebral compliance, blood flow, etc.

## Slide 5: Key Equations
Six intracranial compartments
  Arterial blood (ABV)
  Capillary blood (CBV)
  Venous blood (VBV)
  Cerebral spinal fluid (CSF)
  Brain tissue (BTV)
  Hematoma (HV)
Compartmental pressures
  Pab = ICP + (ABV)/(Arterial Compliance)
  Pcb = ICP + (CBV)/(Capillary Compliance)
  Pvb = ICP + (VBV)/(Venous Compliance)
Intracranial Pressure (ICP)
  ICP = BaseICP  10(Total Cranial Volume–Base Cranial Volume)/PVI

## Slide 6: ICP Dynamic Model

## Slide 7: Modeling an Epidural Hematoma
Simulation parameters
  4th order Runge-Kutta integration
  Fixed step size (30 ms)
Initial conditions
  Dynamic state of equilibrium (steady state flows)
Hematoma
CSF drainage
  Reduces volume in the cranium
  Reduces ICP in turn
  Promotes better blood flow

## Slide 8: Perturbations and Response
Perturbations
  1.0-1.5 min.
    Arterial blood volume drained to hematoma volume
    Fixed rate
  2.0-2.3 min.
    Cerebral spinal fluid drainage
    Fixed rate
Response
  1.0-1.5 min.
    ICP increases
    Venous and arterial blood is forced from the cranial vault
  2.0-2.3 min.
    ICP decreases
    Venous and arterial blood volumes normalize

## Slide 9: Simulation Results

## Slide 10: Clinical Reference Data
Recorded 3 episodes of ICP during CSF drainage
  Traumatic brain injury
  Pediatric intensive care unit (PICU)
  Removed pulsatile component with lowpass filtering
  Sample rate: 1.25 Hz
Following plots omit drainage period

## Slide 11: ICP Before and After CSF Drainage

## Slide 12: Model Calibrated to Fit Clinical Data
24 mL epidural hematoma
6.5 mL CSF drainage
Elevated CSF uptake resistance
  Reduces rate at which ventricles are refilled
  Possibly models impeded flow due to injury or swelling

## Slide 13: Model Run Calibrated to Clinical Event

## Slide 14: Summary
Introduced preliminary model of ICP dynamics
  Uses fluid volumes as state variables, not pressures
Demonstrated modeling of clinical event
  Cerebral spinal fluid (CSF) drain
  Calibrated three parameters to patient
  Observed and modeled ICP transients in good agreement
Model advantages
  Can estimate variables that cannot be clinically measured
  Enables researchers to test hypotheses about multiple potential etiologies